## Slide 1
WAYBIONIC
ENGINEERING SYSTEMS
Ground station software
Operator control · software checks · CAN drive interface · live monitoring
SOFTWARE OVERVIEW
The ROS 2 ground station turns controller input into checked joint commands.
Video and diagnostics remain separate from arm motion.
The carrier link is software-implemented; powered five-drive validation is not documented.
01. SYSTEM ARCHITECTURE
Verified against the ROS 2 paths on main. The hardware connection is coded. It is not powered-validated.
02. TELEOPERATION + INCISION
An Xbox or DualSense controller becomes a 120 Hz stream of
joint setpoints: base, upper, Cartesian, and incision. The
incision group stores the tip pose when selected, then only
inserts, withdraws, or tilts so the tool axis stays on that
point. Sideways homing is blocked while the tip is inserted.
These behaviours run in software on simulated drives, not as
a clinical procedure.
03. COLLISION + JOINT LIMITS
Before a command is sent, the next pose is checked against
the URDF joint ranges and collision boxes on the base,
shoulder, upper arm, forearm, wrist, and tool. A step that
would pass a limit, leave the tip out of reach, or deepen
contact is discarded. The controller rumbles once and the
label names the cause. Ranges on this model are provisional;
the boxes come from the committed meshes, not a live CAD scan.
04. CAN + DRIVE FEEDBACK
The same drive node used in simulation sends MKS SERVO
frames through a UNO R4 carrier: USB serial to a 1 Mbit/s
CAN bus. Replies become joint states. A drive that stops
answering, jumps, or lags its target stops the arm. Real
drives stay still until zeroed, and stop if commands go
silent. The carrier e-stop input is not wired. Software tests
and virtual CAN cover this path. A powered five-drive run is
not in the merged record.
05. DOCTOR VIEW + DIAGNOSTICS
A camera computer stamps each frame and sends JPEG images
over TCP. RViz shows them as Doctor View and reports frame
rate and capture-to-arrival delay. A webcam or a video file
stands in until a procedure camera is chosen. The delay
excludes time in the sensor and on the display. The monitor
lists controller, teleop, drive, bus, and camera health.
Video does not enter the motion-control loop.
06. SOFTWARE VALIDATION
Three results safe to print. Sources rechecked against merged PR descriptions on 27 Oct 2026.
81,421
cases, 0 mismatches
C++ vs Python frames · software only · PR #40
19 + 11
virtual-CAN tests passed
vcan host + four-node · not hardware · PR #45
30 fps
2 ms capture-to-arrival at 1280×720
Test video, not a webcam · PR #36
07. OPERATOR INTERFACE
Real captures from simulated teleop on main (cf3e887), 26 Oct 2026. No generated screenshots.
RViz simulated arm
Cartesian autoplay · simulated drives
Engineering Monitor
Live /diagnostics · simulated teleop
PENDING
Doctor View screenshot
Not captured. A team lead needs to supply a real
RViz frame or an approved test-video capture.
Doctor View — pending
Do not substitute a generated image
WAYBIONIC · SOFTWARE TEAM